## Slide 1
Introduction to Zephyr RTOS with STM32 Microcontrollers
More Than an RTOS
A complete, modular embedded software platform — kernel, drivers, protocol
stacks and libraries — illustrated with the STM32N6 microcontroller
Application
OS Services / Middleware
Kernel
HAL & Drivers · STM32HN6

## Slide 2
Agenda & Presentation Roadmap
Zephyr on STM32 → the VL53L8CX Driver
01
What is Zephyr RTOS?
A scalable, open-source RTOS with layered architecture and hardware abstraction.
02
Architecture & Build Tooling
The layered stack, Devicetree, Kconfig, and the west/CMake pipeline.
03
What is West?
The manifest meta-tool, and our app-as-manifest (T2) topology.
04
Zephyr's Folder Structure
kernel/, arch/, drivers/, boards/, dts/, subsys/ — and Kconfig.
05
What is a Module?
How vendor HALs and our own driver plug into the build via module.yml.
06
Our Workspace Layout
zephyr_app, zephyr/, modules/, bootloader/ — as they actually sit on disk.
07
VL53L8CX Driver Status
Glue vs. vendor architecture, what's shipped, what's still open.
08
Roadmap & Conclusion
Remaining steps to a clean, upstream-ready driver.

## Slide 3
What is Zephyr?
Zephyr on STM32 → the VL53L8CX Driver
■ Linux Foundation governed:
Zephyr is an open-source RTOS hosted by the Linux Foundation, designed to give embedded developers a common software platform
■ Built for small devices:
It can run on tiny, resource-constrained MCUs as well as much more capable processors.
■ Configuration-driven:
Zephyr uses Kconfig and Devicetree to select hardware and software features at build time, keeping the final firmware lean.
■ Broad architecture support: Arm (Cortex-M/A/R), RISC-V, x86, Xtensa and ARC across 800+ evaluated boards.
800+
SUPPORTED BOARDS
20+
CPU ARCHITECTURES
70+
MEMBER COMPANIES
2016
LINUX FOUNDATION PROJECT

## Slide 4
Understanding the Zephyr Architecture
04 / 17
Application
User’s application code (STM32 board apps under zephyr_app/stm32/)
OS Services & Middleware
Networking · USB · BLE · File systems · Modbus · Logging
Kernel
Scheduler · Threads/IPC · Memory & power management
HAL & Device Drivers
Devicetree-described peripheral drivers (incl. st_vl53l8cx)
Board Support Package
Clocks · Memory map · Pinmux · Boot — per Nucleo board
WHY IT MATTERS HERE
Every layer is optional
Build only what your application needs
Every OS-service block : networking, filesystems,
Modbus, crypto — is enabled per project via Kconfig,
so flash and RAM are spent only on what an app
actually uses.
Kernel: Turn off the scheduler if user do not need multithreading.
HAL & Device Driver: Use only the driver your hardware needs. Device tree describes the peripherals and hardware configurations.
Board Support Package: Keep the board-specific details like clock, pinmux, memory map, boot … separate from user’s application.

## Slide 5
Build System & Tooling
Zephyr borrows the Linux kernel's proven configuration model: Device-tree describes the hardware, Kconfig selects the features to build, and west ties sources, SDK and board definitions into one reproducible build.
Devicetree (.dts)
Describes board pins, clocks & peripherals
→
Kconfig
Enables kernel features & libraries (e.g. Modbus, ST_VL53L8CX)
→
App source + CMake
Application logic and build description
CMake + Ninja → zephyr.elf → west flash / west debug
$ west build -b nucleo_h723zg
$ west flash
$ west debug
One command line, any supported board in the workspace — no vendor IDE required.

## Slide 6
What is West: One Command to Manage the Whole Workspace
West manages all the repositories needed by your Zephyr project.
■ One project, many repositories: Zephyr is made up of many repositories, kernel, HALs, libraries, drivers, user’s customized repos etc… West manages them all for the users/developers.
■ west.yaml: tells west what to get, it lists the repositories and the exact version/commits required by the project.
■ Clone once, get the whole workspace: When user clone the application repo, and west uses west.yml to fetch the rest of the required repositories.
■ Unified commands: west init, west update, west build, west flash, west debug , same on every OS.
OUR PROJECT STRUCTURE
zephyr_app is our main repository
It contains
west.yml
Which tell west to fetch:
zephyr/
modules/
bootloader/mcuboot
….
Just clone zephyr_app  run west update  get the complete workspace

## Slide 7
Inside the zephyr/ Core Repository
CORE & ARCHITECTURE
kernel/
Preemptive scheduler, threads, memory slabs, mutexes, IPC.
arch/
CPU ports: ARM Cortex-M/A/R, RISC-V, x86, Xtensa, ARC.
Kconfig
Root build-time feature tree (symbols, dependencies, menus.
HARDWARE & DRIVERS
drivers/
Peripheral & sensor drivers, indexed by class and vendor.
boards/
Board defs, default configs, devicetree overlays, pinmux.
dts/
Devicetree bindings (.yaml) and base SoC .dtsi includes.
SUBSYSTEMS & TESTING
subsys/
BLE host/controller, IP networking, USB, filesystems, logging.
samples/
Ready-to-build example applications.
tests/
Automated Twister test suite across architectures.

## Slide 8
What is a Zephyr Module?
Zephyr on STM32 → the VL53L8CX Driver
■ External source integration: modules let vendor HALs, 3rd-party stacks, crypto libs and sensor SDKs plug into Zephyr's CMake & Kconfig.
■ Declared via zephyr/module.yml: each module names itself and its CMake/Kconfig build hooks.
■ West-managed: most modules are listed in west.yml and cloned/pinned automatically on west update.
■ Our st_vl53l8cx module: listed directly in the root west.yml (remote: github, revision: main) — fully west-managed.
OUR modules/sensor/st_vl53l8cx/zephyr/module.yml
name: st_vl53l8cx
build: cmake: . kconfig: Kconfig settings: {dts_root: .}
MODULE CATEGORIES IN OUR TREE
modules/
hal/ — st, stm32, cmsis, cmsis_6, libmetal
lib/ — zcbor, littlefs, nanopb, openthread,
lvgl, hostap, picolibc
crypto/ — mbedtls, mbedtls-3.6,
tf-psa-crypto, mldsa-native
fs/ — fatfs, littlefs
debug/ — segger, percepio, mipi-sys-t
tee/ — tf-a, tf-m
sensor/st_vl53l8cx — our custom driver

## Slide 9
Top-Level Layout: zephyr_dev/
zephyr_app/
MANIFEST REPO
Owns west.yml. STM32 app code per board: nucleo_f401re, nucleo_g474re, nucleo_h723zg, nucleo_l432kc, nucleo_n657x0_q, mp2_m33.
zephyr/
UPSTREAM CORE
Pulled by west update from zephyrproject-rtos/zephyr, pinned to an exact commit.
modules/
VENDOR HAL & LIBS
hal/, lib/, crypto/, fs/, debug/, tee/, sensor/st_vl53l8cx — each an independent git repo.
bootloader/mcuboot
SECURE BOOT
Pulled by west update, gated by the workspace's bootloader group-filter.
pc_application/, pc_tools/
HOST COMPANIONS
A C ranging server and a Qt-based vl53l8_viewer app for the ToF sensor.

## Slide 10
modules/ Is a Folder of Repositories
It is simply a folder containing many independent repositories:
modules/hal/stm32/
modules/hal/cmsis/
modules/lib/openthread/
modules/crypto/mbedtls/
modules/sensor/st_vl53l8cx/
West manages these repositories
clones  updates  checksout the required version for each module
WORKSPACE AUDIT SNAPSHOT
hal/st ✓ hal/stm32 ✓ hal/cmsis ✓ lib/openthread ✓ crypto/mbedtls ✓ sensor/st_vl53l8cx ✓
A REAL EXAMPLE: VL53L8CX
st_vl53l8cx status
Before:
st_vl53l8cx was manually placed in the workspace
NOW:
modules/sensor/st_vl53l8cx/
✅ Independent Git repository ✅ Listed in west.yml ✅ West clones and manages it ✅ Version/commit is controlled by the manifest

## Slide 11
Zephyr vs. a Classic RTOS Approach
Capability
Bare-metal + Vendor HAL
Classic RTOS (FreeRTOS)
Zephyr
Scheduler & IPC
Manual (user has to do)
Yes
Yes + memory protection, power mgmt
Driver model / BSP
Vendor HAL, per-MCU
Often different for each
MCU
Common Driver Model
Networking / BLE / USB
User has to add and
Integrate separately
User has to add and
Integrate separately
Native, in-tree, tested together
Fieldbus (Modbus, CAN)
Manually add a library (third party)
In-tree Modbus & CAN subsystems
Config & build system
Vendor IDE / tools
Vendor IDE / tools
Kconfig + Devicetree + west/CMake
Zephyr brings the RTOS, drivers, middleware and build system together
Manually add a library (third party)

## Slide 12
Performance: STM32Cube HAL vs. ST Low-Layer in Zephyr
Cost of the same I²C operation in each driver layer — cycles are CPU work, not bus time (NUCLEO-F401RE @ 84 MHz)
LL_I2C_TransmitData8() is one opcode: MODIFY_REG(I2Cx->DR, I2C_DR_DR, Data); → strb r1, [r0, #16] Footprint per peripheral: 2.5–4.0 KB Flash and 48–64 B stack per HAL call, vs 400–800 B and zero stack for inlined LL macros.
Sources: ST UM1785 / UM1850; Zephyr i2c_stm32.c; NUCLEO-F401RE + X-NUCLEO-53L8A1 shield.
Operation | STM32Cube HAL call | Zephyr + ST LL call | Gain
Write one byte | HAL_I2C_Master_Transmit() — 120–250 CPU cycles of driver overhead per byte | LL_I2C_TransmitData8() — compiles to 1 opcode (12–24 ns) | ~150x less CPU work
Check a status flag | I2C_WaitOnFlagUntilTimeout() + HAL_GetTick() on every byte | LL_I2C_IsActiveFlag_TXE() — one register read | No polling loop
Handle the interrupt | HAL_I2C_EV_IRQHandler() — branchy, 80–150 cycles | i2c_stm32_isr() — fixed 5–10 cycles | > 15x faster, jitter-free
Wait for completion | Blocking timeout loop — CPU pinned at ~98% | k_sem_take() — thread sleeps, CPU < 1% | > 95% CPU freed
Send the 32 KB firmware | HAL_I2C_Mem_Write() — ~740 ms of busy-wait | i2c_write_dt() — same 740 ms on the bus, < 0.6 ms of CPU | Bus-bound, not CPU-bound

## Slide 13
VL53L8CX Driver Development
A clean, production-grade Zephyr sensor driver for STMicroelectronics' 8x8 multizone direct Time-of-Flight (dToF) ranging sensor.
12 / 17

## Slide 14
VL53L8CX DRIVER
VL53L8CX : Adding Multizone ToF Support to Zephyr
A sensor family that currently has no native Zephyr driver
■ ST VL53L8CX 8x8 multizone ToF: VL53L8CX provides 64 ranging zones, giving us much more spatial information than a single-zone distance sensor.
■ Existing Zephyr single-zone drivers: VL53L0X and VL53L1X only — both single-zone, older sensors.
■ Zero multizone support in Zephyr: no driver anywhere in git history for VL53L5/7/8/9CX.
■ So we built one: The goal is to bring the VL53L8CX into the Zephyr sensor framework and make it usable like other Zephyr sensors.
Why it is useful
High upstream potential
No VL53L5/7/8/9CX driver exists upstream, so this is not duplicated work.
New multizone use cases
64 zones enable gesture, presence and obstacle mapping.
Standard sensor API
Fetch/get calls behave like any other Zephyr sensor, configured from devicetree.

## Slide 15
VL53L8CX Driver Architecture — Our Code vs. ST Code
1. Zephyr Application
sensor_sample_fetch() · sensor_channel_get()
Uses the standard Zephyr sensor API instead of talking to the VL53L8CX directly — one common interface for every sensor driver.
2. Our Zephyr Driver
vl53l8cx.c · platform.c · Devicetree · Kconfig
Our code — translates Zephyr sensor API ↔ ST's VL53L8CX API.
3. ST Vendor Code
vl53l8cx_api.c
ST's ranging algorithms and device-specific implementation — we don't modify it.
4. Hardware
VL53L8CX · I²C · LPn · INT
I²C for data, LPn for power control, INT for data-ready.
CORE PRINCIPLE
Strict separation of concerns
1. Glue layer (vl53l8cx.c & platform.c) — ours to write and maintain, Apache-2.0.
2. Vendor ULD (uld/vl53l8cx_api.c) must stay 100% pristine ST code (BSD-3-Clause) — no Zephyr #includes or printk().

## Slide 16
VL53L8CX DRIVER
Status Update: Then vs. Now
Zephyr on STM32 → the VL53L8CX Driver
FIXED SINCE THE LAST REVIEW
✓
module.yml, Kconfig, CMakeLists.txt
Fully populated, no longer empty stubs.
✓
Devicetree binding written
dts/bindings/sensor/st,vl53l8cx.yaml now exists.
✓
Sample app builds on 2 boards
vl53l8cx_simple, overlays for G474RE & N657X0-Q.
✓
Real version control
Proper git repo, 2 commits, ~2,460 lines of code.
STILL OPEN
✗
Polluted vendor source
uld/vl53l8cx_api.c still has a #include and 6 printk() debug calls hand-spliced in.
✗
Missing LICENSE file
No LICENSE ships with uld/, only a bare ST copyright comment.

## Slide 17
VL53L8CX DRIVER
Remaining Steps to Production
01
Clean the Vendor Source File
Strip the stray #include and printk() calls from uld/vl53l8cx_api.c; move diagnostics into platform.c / vl53l8cx.c via LOG_DBG().
02
Attach Licensing & Copyright
Ship ST's official BSD-3-Clause LICENSE alongside uld/, and align copyright headers with it.
03
Validate on the Hardware Matrix
Build, flash and run automated I2C ranging checks across Nucleo-G474RE, Nucleo-N657X0-Q and STM32MP257F.
04
Decide the Upstream Path
Iterate as a unified out-of-tree module, or split into Zephyr-tree glue + a hal_st contribution for upstream submission.

## Slide 18
CONCLUSION
One Platform, One Workspace, One Driver Away
The same west build and driver model take a Nucleo board from blinky to the VL53L8CX ranging driver — and the driver itself is close: build system done, licensing and vendor-source hygiene are what remain.
Not just a scheduler
Kernel + OS services + libraries + drivers, versioned together.
A real ecosystem gap
No multizone dToF driver exists upstream — ours is the first.
Nearly production-ready
Build system complete; vendor-source cleanup is the last mile.
zephyrproject.org · docs.zephyrproject.org · github.com/zephyrproject-rtos/zephyr
Workspace location: zephyr_dev/modules/sensor/st_vl53l8cx