## Slide 1
ZEPHYR RTOS · WEST · MODULES
Zephyr Workspace Architecture
& the VL53L8CX ToF Sensor Driver
How Zephyr, West and modules fit together — and where our ST VL53L8CX
sensor driver development stands today.
zephyr_dev workspace overview
Sept 2026

## Slide 2
OVERVIEW
Agenda
02 / 15
Zephyr Workspace & VL53L8CX Driver
01
What is Zephyr?
A scalable, open-source RTOS for embedded & IoT
02
What is West?
Zephyr's multi-repo meta-tool
03
Zephyr's folder structure
kernel, arch, drivers, boards, modules
04
What is a Module?
How external/vendor code plugs into Zephyr
05
Our workspace layout
zephyr_dev: zephyr_app, zephyr, modules, bootloader
06
VL53L8CX driver development
Status, architecture, licensing, next steps

## Slide 3
INTRODUCTION
What is Zephyr?
03 / 15
Zephyr Workspace & VL53L8CX Driver
● A small-footprint, open-source RTOS for resource-constrained & IoT devices
– Hosted by the Linux Foundation — vendor-neutral, permissively licensed (Apache-2.0)
● Scales from tiny single-core MCUs to multicore application processors
● Configuration-driven design
– Kconfig — build-time feature/driver selection (like the Linux kernel)
– Devicetree (DTS) — hardware description, decoupled from driver code
● Broad hardware support out of the box
– Architectures: Arm (M/A/R), RISC-V, x86, Xtensa, ARC, SPARC
– 600+ boards, dozens of vendor HALs, hundreds of drivers
● Rich built-in subsystems: Bluetooth/BLE, networking (IP stack), USB, filesystems, logging, power management, sensors
WHY IT MATTERS HERE
Our STM32 boards (Nucleo-G474RE, Nucleo-N657X0-Q, STM32MP257F-DK) all build on the same Zephyr core — the RTOS, build system and sensor API are identical across every target; only the board files and HAL differ.

## Slide 4
INTRODUCTION
What is West?
04 / 15
Zephyr Workspace & VL53L8CX Driver
● Zephyr's own meta-tool for managing a multi-repository workspace
– Similar goal to git submodules — but purpose-built for Zephyr's scale
● Reads a manifest file: west.yml
– Lists every repo (Zephyr core, HAL modules, bootloader...) and its pinned revision
– One repo is the “manifest repository” — the thing you actually clone first
● Key commands
– west init → set up a new workspace from a manifest
– west update → clone/checkout every project at its pinned revision
– west build / west flash / west debug → build & run on target
OUR TOPOLOGY: “APP AS MANIFEST” (T2)
zephyr_app is our manifest repo
(the only thing we actually clone)
west.yml inside it lists:
• zephyr (core RTOS)
• modules/* (HALs, libs, crypto...)
• bootloader/mcuboot
west update pulls all of the above
as siblings of zephyr_app/

## Slide 5
ZEPHYR INTERNALS
Inside the zephyr/ Repository
05 / 15
Zephyr Workspace & VL53L8CX Driver
zephyr/
├─ kernel/ core: scheduler, threads, memory, IPC primitives
├─ arch/ CPU architecture support: arm, arm64, riscv, x86...
├─ boards/ per-board config, devicetree, defconfig
├─ drivers/ peripheral & sensor drivers, by class then vendor
│ └─ sensor/st/vl53l1x, vl53l0x, lsm6dsl, ...
├─ dts/ devicetree bindings & base .dtsi files
├─ subsys/ Bluetooth, networking, USB, fs, logging...
├─ samples/ ready-to-build example applications
├─ tests/ Twister test suite
└─ Kconfig root of the build-time configuration tree

## Slide 6
ZEPHYR INTERNALS
What is a “Module”?
06 / 15
Zephyr Workspace & VL53L8CX Driver
● External source code integrated into the Zephyr build
– Vendor HALs, third-party libraries, crypto, filesystems, sensor SDKs
● Declared with a zephyr/module.yml manifest file
– name:, and build: { cmake, kconfig, cmake-ext, kconfig-ext }
– Tells west/CMake/Kconfig “here is more source + config to pull in”
● Two ways a module reaches the build
– West-managed — listed in a manifest, auto-cloned by west update
– Out-of-tree / ZEPHYR_EXTRA_MODULES — pointed at manually, e.g. our own driver
TYPICAL module.yml
name: hal_st
build:
cmake-ext: True
kconfig-ext: True
Module categories seen in our
workspace's modules/ folder:
hal, lib, crypto, fs, debug, tee, sensor

## Slide 7
OUR WORKSPACE
Top-Level Layout: zephyr_dev/
07 / 15
Zephyr Workspace & VL53L8CX Driver
zephyr_dev/ <- workspace root
├─ zephyr_app/ MANIFEST repo (west topdir) — owns west.yml
├─ zephyr/ core RTOS, pulled by west from zephyrproject-rtos
├─ modules/ vendor HALs & libraries, pulled by west
│ ├─ hal/ st, stm32, cmsis, nordic, nxp, ti, ...
│ ├─ lib/ openthread, zcbor, littlefs, open-amp, ...
│ ├─ crypto/ mbedtls, tf-psa-crypto, ...
│ ├─ fs/, debug/, tee/, bsim_hw_models/
│ └─ sensor/ st_vl53l8cx <- OUR module (not west-managed yet)
└─ bootloader/
└─ mcuboot/ pulled via zephyr's own manifest

## Slide 8
OUR WORKSPACE
modules/ is a Folder, Not a Repo
08 / 15
Zephyr Workspace & VL53L8CX Driver
● Every subfolder under modules/ is its own independent git clone
– modules/hal/nordic → github.com/zephyrproject-rtos/hal_nordic
– modules/hal/st → github.com/zephyrproject-rtos/hal_st
– modules/lib/openthread → github.com/zephyrproject-rtos/openthread
● west update clones ~50 such repos at the revisions pinned in west.yml
● The one exception in our tree:
– modules/sensor/st_vl53l8cx has NO .git directory
– Not listed in any manifest — west never touched it
– It was placed there by hand; it only looks like a managed module
VERIFIED IN THIS WORKSPACE
hal/st
✓ git repo
hal/stm32
✓ git repo
hal/nxp, hal/ti, ...
✓ git repo
sensor/st_vl53l8cx
✗ no .git

## Slide 9
PART TWO
VL53L8CX Driver Development
Building a Zephyr sensor driver for ST's 8x8 multizone Time-of-Flight sensor

## Slide 10
VL53L8CX
The Sensor & the Gap in Zephyr
10 / 15
Zephyr Workspace & VL53L8CX Driver
● VL53L8CX: ST direct Time-of-Flight (dToF) 8x8 multizone ranging sensor
– I2C, up to 64 independent distance zones, configurable resolution/frequency
● Zephyr already supports two ST ToF sensors
– VL53L0X — drivers/sensor/st/vl53l0x (single zone)
– VL53L1X — drivers/sensor/st/vl53l1x (single zone, longer range)
● The newer 8x8 multizone family has NO Zephyr driver at all
– Confirmed: no VL53L5CX / L7CX / L8CX / L9CX anywhere in Zephyr's git history
– No open community PR for this family either
REAL GAP, REAL VALUE
Building this driver isn't duplicating existing work — the 8x8 multizone dToF family genuinely has no Zephyr support today. A clean, working driver here has real upstream value once it's mature.

## Slide 11
VL53L8CX
Architecture: Glue Driver vs. Vendor Code
11 / 15
Zephyr Workspace & VL53L8CX Driver
Zephyr Application
sensor_sample_fetch(dev) / sensor_channel_get(dev, ...)
Zephyr Sensor API Layer — vl53l8cx.c
devicetree, sensor_driver_api, struct device, Kconfig
GLUE — platform.c
translates ST's abstract I/O calls into real i2c_write_read_dt() / k_msleep()
Vendor ULD API — uld/vl53l8cx_api.c
ST's ranging algorithm & register maps — knows nothing about Zephyr
I2C bus / GPIO pins
physical hardware
KEY IDEA
The glue is ours to write and modify freely.
The vendor ULD must stay pristine — it's ST's licensed code, not ours to edit.

## Slide 12
VL53L8CX
The Existing Precedent: VL53L1X
12 / 15
Zephyr Workspace & VL53L8CX Driver
Zephyr never mixes vendor SDK code into its own tree — it always splits across two repositories:
zephyr/drivers/sensor/st/vl53l1x/
• vl53l1.c Zephyr sensor API glue
• vl53l1_platform.c I2C/GPIO wrapper
License: Apache-2.0
Owned & reviewed by: Zephyr sensor
subsystem maintainers
modules/hal/st (hal_st repo)
• sensor/vl53l1x/api/core/src/vl53l1_api.c
+ calibration, wait, core, preset-modes...
License: GPL-2.0+ OR BSD-3-Clause (ST's choice)
Owned & reviewed by: ST / hal_st maintainers
This is the target shape for VL53L8CX too — our vl53l8cx.c/platform.c = future glue, our uld/ = future hal_st contribution.

## Slide 13
VL53L8CX
What We Verified So Far
13 / 15
Zephyr Workspace & VL53L8CX Driver
CONFIRMED
✓
Vendor uld/*.c source diffed against stm32duino/VL53L8CX (official ST ULD port) — confirmed genuine, algorithmically identical
✓
Licensing: ST's ULD driver family is BSD-3-Clause — compatible with Zephyr's accepted license list
✓
Fills a real gap: no VL53L5/7/8/9CX driver exists anywhere in Zephyr
STILL BLOCKING
✗
module.yml, Kconfig and CMakeLists.txt are empty — module does not build yet
✗
uld/vl53l8cx_api.c has debug printk()s + a Zephyr #include hand-spliced into vendor source
✗
No LICENSE file shipped alongside the vendor code; copyright header uses a placeholder “Zephyr Community”
✗
Not under version control at all — no git repo, no history, no attribution trail

## Slide 14
VL53L8CX
Next Steps
14 / 15
Zephyr Workspace & VL53L8CX Driver
1
Clean the vendor file
Restore uld/vl53l8cx_api.c to a pristine ST copy; move debug diagnostics into platform.c/vl53l8cx.c behind LOG_DBG
2
Make it buildable
Fill in module.yml, Kconfig, CMakeLists.txt (root + driver level), and the devicetree binding (st,vl53l8cx.yaml)
3
Fix licensing hygiene
Attach ST's real LICENSE file; replace the placeholder copyright header with correct attribution
4
Validate on hardware
Build & test across target boards (Nucleo-G474RE, Nucleo-N657X0-Q, ...) before trusting any “verified” claim
5
Decide on structure
Keep as one module for now; split into glue vs. vendor subtrees only once ready to propose it upstream

## Slide 15
Thank You
Questions & discussion
zephyr_dev workspace — modules/sensor/st_vl53l8cx