## Slide 1
ZEPHYR RTOS · WEST · MODULES
Zephyr Workspace Architecture & the VL53L8CX ToF Sensor Driver
How Zephyr, West, and external modules fit together — and where our STMicroelectronics VL53L8CX 8x8 multizone driver development stands today.
zephyr_dev workspace overview
September 2026

## Slide 2
OVERVIEW
Agenda & Presentation Roadmap
Zephyr Workspace & ST VL53L8CX Driver Architecture
02 / 15
01
What is Zephyr RTOS?
A scalable, open-source RTOS for modern embedded & IoT devices with hardware abstraction and rich subsystems.
02
What is West?
Zephyr's multi-repository meta-tool for orchestrating manifests, cloning dependencies, and building images.
03
Zephyr's Folder Structure
Deep dive into kernel/, arch/, drivers/, boards/, subsys/, and Kconfig organization.
04
What is a Module?
How external vendor SDKs and HALs plug seamlessly into the Zephyr build via module.yml.
05
Our Workspace Layout
Top-level architecture of zephyr_dev: zephyr_app, zephyr core, modules, and bootloader.
06
VL53L8CX Driver Development
Current status, glue vs. vendor architecture, licensing hygiene, and verified next steps.

## Slide 3
INTRODUCTION
What is Zephyr RTOS?
Zephyr Workspace & ST VL53L8CX Driver Architecture
03 / 15
■ Linux Foundation Governed: Open-source, vendor-neutral RTOS with permissive Apache-2.0 licensing, backed by major industry leaders.
■ Massive Scalability: Operates efficiently on ultra-low-power single-core MCUs up to high-performance multicore 64-bit MPUs.
■ Configuration-Driven: Kconfig provides build-time modular selection, while Devicetree (DTS) completely decouples hardware topology from driver logic.
■ Broad Architecture Support: Arm (Cortex-M/A/R), RISC-V, x86, Xtensa, and ARC across 600+ evaluated boards.
■ Production-Ready Subsystems: Built-in Bluetooth LE, complete IPv4/IPv6 networking stack, USB host/device, flash filesystems, power management, and standardized sensor APIs.
WHY IT MATTERS HERE
Target Portability
Our STM32 hardware targets build on the exact same Zephyr RTOS foundation: • Nucleo-G474RE (Cortex-M4) • Nucleo-N657X0-Q (Cortex-M55 + NPU) • STM32MP257F-DK (Dual A35 + M33) The build system, driver APIs (sensor_driver_api), and application code remain 100% identical; only the device tree overlay and vendor HAL change.

## Slide 4
INTRODUCTION
What is West? (Zephyr's Meta-Tool)
Zephyr Workspace & ST VL53L8CX Driver Architecture
04 / 15
■ Multi-Repository Meta-Tool: Zephyr's dedicated management CLI — solving multi-repo dependency orchestration cleaner than git submodules.
■ Manifest-Driven Workflow: Driven by west.yml: securely specifies all upstream repositories (Zephyr kernel, HALs, libraries) and their exact pinned git SHA revisions.
■ Manifest Repository Concept: The central entry-point repository that holds west.yml. Cloning this single repo allows West to reconstruct the entire multi-gigabyte ecosystem.
■ Unified Development Commands: Standardized commands across all OS platforms: west init, west update, west build, west flash, and west debug.
OUR TOPOLOGY: APP-AS-MANIFEST (T2)
zephyr_app owns west.yml
zephyr_app is our manifest repo (the only repository cloned initially). west.yml directs west update to fetch siblings into the root: • zephyr/ (core RTOS kernel) • modules/hal/* (ST, CMSIS, etc.) • modules/lib/* (crypto, POSIX) • bootloader/mcuboot Keeps proprietary application code separated from upstream open-source code.

## Slide 5
ZEPHYR INTERNALS
Inside the zephyr/ Core Repository
Zephyr Workspace & ST VL53L8CX Driver Architecture
05 / 15
Core & Architecture
kernel/ Core OS: preemptive scheduler, thread management, memory slabs, mutexes, semaphores, and IPC queues.
arch/ CPU architecture ports: ARM Cortex-M/A/R, RISC-V, x86, Xtensa, ARC, SPARC exception handling.
Kconfig Root build-time feature configuration tree (symbols, dependencies, menus).
Hardware & Drivers
drivers/ Hardware peripheral and sensor drivers indexed by class and vendor (e.g. sensor/st/vl53l1x).
boards/ Board definitions, default configurations, hardware devicetree overlays, and pin muxes.
dts/ Devicetree bindings (.yaml) defining hardware properties and base SOC include files (.dtsi).
Subsystems & Testing
subsys/ Higher-level stacks: Bluetooth/BLE host & controller, IP networking, USB, filesystems, logging.
samples/ Ready-to-build example applications demonstrating peripheral & protocol usage.
tests/ Comprehensive automated Twister test suite ensuring code quality across architectures.

## Slide 6
ZEPHYR INTERNALS
What is a Zephyr Module?
Zephyr Workspace & ST VL53L8CX Driver Architecture
06 / 15
■ External Source Integration: Modules allow external code (vendor HALs, 3rd-party stacks, crypto libraries, sensor SDKs) to seamlessly integrate into Zephyr's CMake & Kconfig build system.
■ Declared via zephyr/module.yml: Every module contains a manifest file defining its module name, CMake hooks (cmake:, cmake-ext:), and Kconfig hooks (kconfig:, kconfig-ext:).
■ West-Managed Modules: Listed directly inside west.yml — automatically cloned, updated, and pinned to specific revisions during west update.
■ Out-of-Tree Modules (ZEPHYR_EXTRA_MODULES): Custom, in-development, or proprietary modules plugged into the build without needing an upstream west.yml entry.
TYPICAL zephyr/module.yml
name: hal_st build: cmake-ext: True kconfig-ext: True settings: dts_root: .
MODULE CATEGORIES IN OUR TREE
• hal/ (st, stm32, cmsis, nordic, nxp, ti) • lib/ (openthread, zcbor, littlefs, open-amp) • crypto/ (mbedtls, tf-psa-crypto) • sensor/ (st_vl53l8cx — our custom driver)

## Slide 7
OUR WORKSPACE
Top-Level Workspace Layout: zephyr_dev/
Zephyr Workspace & ST VL53L8CX Driver Architecture
07 / 15
zephyr_app/ [MANIFEST REPOSITORY (Topdir)]
Owns west.yml. The only repository cloned directly by the engineer. Contains all target application code and board overlays.
zephyr/ [UPSTREAM CORE RTOS KERNEL]
Fetched by West from zephyrproject-rtos/zephyr. Contains scheduler, architecture ports, core subsystem APIs, and built-in drivers.
modules/ [VENDOR HALS & THIRD-PARTY LIBS]
Subdivided into hal/ (st, cmsis), lib/ (openthread), crypto/ (mbedtls), fs/. Each folder is an independent upstream git repository.
modules/sensor/st_vl53l8cx [OUR CUSTOM SENSOR DRIVER MODULE]
Our driver under development for ST's 8x8 multizone dToF sensor. Currently an out-of-tree module folder.

## Slide 8
OUR WORKSPACE
modules/ is a Folder, Not a Repository
Zephyr Workspace & ST VL53L8CX Driver Architecture
08 / 15
■ Collection of Independent Repos: modules/ itself is just a local filesystem directory. Every subdirectory inside it is an independent git repository cloned from GitHub.
■ West Management Mechanics: west update inspects west.yml and automatically clones ~50 individual repositories at exact pinned revisions into modules/hal/, modules/lib/, etc.
■ The Hand-Placed Exception: modules/sensor/st_vl53l8cx is NOT managed by West. It contains no .git folder and was placed manually in the workspace tree.
WORKSPACE AUDIT STATUS
modules/hal/st
✓ Git Repo
modules/hal/stm32
✓ Git Repo
modules/hal/cmsis
✓ Git Repo
modules/lib/openthread
✓ Git Repo
modules/crypto/mbedtls
✓ Git Repo
modules/sensor/st_vl53l8cx
✗ No .git folder

## Slide 9
PART TWO
VL53L8CX Driver Development
Building a clean, production-grade Zephyr sensor driver for STMicroelectronics' 8x8 multizone direct Time-of-Flight (dToF) ranging sensor.

## Slide 10
VL53L8CX DRIVER
The Sensor & The Ecosystem Gap in Zephyr
Zephyr Workspace & ST VL53L8CX Driver Architecture
10 / 15
■ ST VL53L8CX 8x8 Multizone dToF: Advanced optical time-of-flight sensor delivering up to 64 independent ranging zones across a wide 65° diagonal FOV with up to 4-meter range.
■ Existing Zephyr Single-Zone Drivers: Zephyr currently contains drivers for older single-zone ST ToF sensors: • VL53L0X (drivers/sensor/st/vl53l0x — single zone, short range) • VL53L1X (drivers/sensor/st/vl53l1x — single zone, long range)
■ Zero Multizone Support in Zephyr: Zephyr has NO existing driver anywhere in git history for the multizone dToF family (VL53L5CX, VL53L7CX, VL53L8CX, VL53L9CX).
■ No Open Upstream Pull Requests: Confirmed: no community or vendor PR currently exists for this family in Zephyr.
REAL GAP · REAL VALUE
High Upstream Potential
Building this driver is not duplicating existing community efforts — the 8x8 multizone dToF family genuinely lacks Zephyr support today. A clean, robust, well-architected driver here delivers immediate project capability and holds high potential for upstream acceptance by the Zephyr sensor subsystem maintainers.

## Slide 11
VL53L8CX DRIVER
Architecture: Glue Driver vs. Vendor Code
Zephyr Workspace & ST VL53L8CX Driver Architecture
11 / 15
Zephyr Application Layer
Calls standard sensor_sample_fetch(dev) and sensor_channel_get(dev, ...)
Zephyr Sensor Subsystem · vl53l8cx.c
Implements sensor_driver_api, Devicetree binding resolution, and Kconfig integration
Hardware Glue Layer · platform.c [OUR CODE]
Translates ST's abstract I/O calls to Zephyr i2c_write_read_dt(), GPIO controls & k_msleep()
Vendor ULD Library · uld/vl53l8cx_api.c [PRISTINE ST CODE]
ST's raw ranging algorithms, firmware loader, and register maps — 100% agnostic of Zephyr
Physical Hardware Layer · I2C / SPI & Interrupts
ST VL53L8CX sensor, I2C/SPI bus lines, LPn power pins, and INT GPIO interrupts
CORE PRINCIPLE
Strict Separation of Concerns
1. Glue Layer (vl53l8cx.c & platform.c) Ours to write, optimize, and maintain freely under Apache-2.0. 2. Vendor ULD (uld/vl53l8cx_api.c) Must remain 100% pristine ST licensed code (BSD-3-Clause). Zero Zephyr-specific #includes or printk() statements allowed inside vendor source.

## Slide 12
VL53L8CX DRIVER
The Existing Upstream Precedent: VL53L1X
Zephyr Workspace & ST VL53L8CX Driver Architecture
12 / 15
Zephyr never mixes vendor SDK code directly into its kernel tree — it cleanly splits drivers across two repositories:
zephyr/drivers/sensor/st/vl53l1x/ (Zephyr Tree)
• vl53l1.c — Zephyr sensor API glue implementation • vl53l1_platform.c — I2C & GPIO bus wrappers • Kconfig & CMakeLists.txt — driver configuration License: Apache-2.0 (standard Zephyr permissive) Owned & Reviewed by: Zephyr sensor subsystem maintainers
modules/hal/st/ (hal_st Module Repo)
• sensor/vl53l1x/api/core/src/vl53l1_api.c • vl53l1_api_calibration.c, vl53l1_api_core.c, ... • STMicroelectronics raw sensor algorithms & register maps License: BSD-3-Clause / GPL-2.0+ (ST official license) Owned & Reviewed by: STMicroelectronics & hal_st maintainers
Target Blueprint for VL53L8CX: Our vl53l8cx.c and platform.c will serve as the upstream Zephyr sensor glue, while our uld/ folder will be submitted upstream to modules/hal/st.

## Slide 13
VL53L8CX DRIVER
Driver Audit: Confirmed Findings vs. Current Blockers
Zephyr Workspace & ST VL53L8CX Driver Architecture
13 / 15
CONFIRMED & READY
✓
Genuine ST ULD Source Code
Vendor uld/*.c source diffed against official stm32duino/VL53L8CX repository — verified genuine and algorithmically identical.
✓
License Compatibility
ST's ULD driver family is BSD-3-Clause licensed — 100% compatible with Zephyr Project licensing requirements.
✓
High-Value Ecosystem Gap
Fills a true void: no VL53L5/7/8/9CX multizone driver exists anywhere in Zephyr today.
CURRENT BLOCKERS & DEFECTS
✗
Empty Build Files
module.yml, Kconfig, and CMakeLists.txt are empty stubs — the module does not currently build in Zephyr.
✗
Polluted Vendor Source
uld/vl53l8cx_api.c contains debug printk() calls and a Zephyr #include hand-spliced into vendor code.
✗
Missing License File & Attribution
No LICENSE file shipped alongside vendor code; header uses placeholder 'Zephyr Community'.
✗
No Version Control History
Not under git control — no repository, no commit history, and no attribution trail.

## Slide 14
VL53L8CX DRIVER
Execution Roadmap: Next Steps to Production
Zephyr Workspace & ST VL53L8CX Driver Architecture
14 / 15
01
Clean the Vendor Source File
Restore uld/vl53l8cx_api.c to a 100% pristine ST release copy. Relocate all debug diagnostics into platform.c and vl53l8cx.c using standard Zephyr LOG_DBG().
02
Make the Driver Module Buildable
Populate zephyr/module.yml, Kconfig, CMakeLists.txt (root + driver levels), and complete the formal devicetree binding YAML (st,vl53l8cx.yaml).
03
Fix Licensing & Copyright Hygiene
Attach ST's official BSD-3-Clause LICENSE file to uld/ and replace placeholder copyright headers with accurate author & license attributions.
04
Validate on Physical Target Hardware
Build, flash, and execute across our hardware test matrix (Nucleo-G474RE, Nucleo-N657X0-Q, STM32MP257F) with automated I2C ranging checks.
05
Decide on Long-Term Upstream Architecture
Maintain as an unified out-of-tree module for rapid internal iteration; split into Zephyr tree glue + hal_st contribution when submitting upstream.

## Slide 15
Thank You
Open for Questions, Technical Discussion & Hardware Validation
Workspace Location: zephyr_dev/modules/sensor/st_vl53l8cx